## Slide 1: ClearOne DARE™ Feedback Eliminator (FBE)
PROFESSIONAL AUDIO

## Slide 2: DARE Feedback Eliminator (FBE)
We know it when we hear it!
  Click the speaker icon for a reminder.
Feedback occurs when:
  An amplified sound re-enters a sound system…
  Through any open microphone, and…
  Is amplified again and again
Ringing occurs when:
  An amplified frequency of sound re-enters a sound system…
  Through any open microphone, and…
  Is amplified for a period of time
What is Feedback and Ringing?

## Slide 3
Technicians must tune the system
    Slowly raise and test reinforcement systems
    Carefully remove and/or insert equalization filtering
Tuning is a 100% manual exercise!
Re-tuning is required after each subsequent change to the room environment
How do we combat feedback?
DARE Feedback Eliminator (FBE)
Without a Feedback Eliminator
There is a better way…
Notes: Note: Manual equalization to remove feedback is a time intensive process of raising gain in the system, monitoring feedback that arises and notching offending frequencies repeatedly.
Note: Fixed nodes are assigned during first setup, Dynamic nodes are added automatically during system operation.
Note: DARE FBE fully automates this process and also provides continuing feedback protection as the system operates.
Note: Up to 16 Nodes per FBE Process

## Slide 4
Removes feedback and ringing
Automatically determines and implements the optimal filter settings
Continuously monitors audio and adjusts for new room conditions
Gives the total system gain an additional boost of up to 8 dB
How do we combat feedback?
DARE Feedback Eliminator (FBE)
The DARE Feedback Eliminator
Notes: Note: Manual equalization to remove feedback is a time intensive process of raising gain in the system, monitoring feedback that arises and notching offending frequencies repeatedly.
Note: Fixed nodes are assigned during first setup, Dynamic nodes are added automatically during system operation.
Note: DARE FBE fully automates this process and also provides continuing feedback protection as the system operates.
Note: Up to 16 Nodes per FBE Process

## Slide 5
Contributes to an effective meeting environment
  Removes feedback and ringing that are extremely disruptive
Saves time, saves money
  Automates a task that requires hours for a trained acoustician to complete
Provides high quality audio
  The DARE feedback eliminator is unsurpassed.
  In combination with FiBeam™ and DsBeam™ of the BMA 360, creates the absolute best voice lift system in the industry
Why is the DARE FBE valuable?
DARE Feedback Eliminator (FBE)
The Value of the DARE FBE
Notes: Note: FiBeam = Frequency Invariant Beam technology (reference polar pattern graphic). Ideal for consistent Lift behavior.
Note: DsBeam = Deep Sidelobe Beam technology. Ideal for maximum Lift gain and out of lobe noise and/or feedback rejection.

## Slide 6
Prevents feedback damage to equipment and amplifiers
The DARE FBE, in combination with the BMA 360’s beamforming, integrated DSP and Voice Lift, enables the auto setup and dynamic monitoring.
An advantage over the competition - no one else has this unsurpassed combination of advanced technologies.
Why is the DARE FBE valuable?
+
=
Unsurpassed Audio Performance and Reduced Cost!
DARE Feedback Eliminator (FBE)
And More Value
Notes: Note: Dynamic FeedBack Elimination, such as DARE, is a huge benefit when working with Beamforming microphones such as the BMA360.

## Slide 7
Automatic Setup
  Finds fixed filters that eliminate feedback
  Stores fixed filters in DSP memory
Dynamic Filters
  Continuously monitors for new feedback and ringing
  Adds filters in 3 dB increments to a max depth of 12 dB
Up to 16 total filters per FBE, allocated between Fixed and Dynamic
Ringing Elimination for increased stability
How does the DARE™ Feedback Eliminator (FBE) Work?
DARE Feedback Eliminator (FBE)
Notes: Note: If more than 12 dB is required at a frequency band, it adds a second filter starting at 3 dB.
Note: Fixed filters are added during Automated Setup. Dynamic filters are added automatically during normal operation.

## Slide 8
With any CONVERGE Pro 2 DSP
Via CONSOLE AI > Processing Block Properties
Offline mode – partial functionality
Online mode – full functionality
How can the DARE FBE be used?
DARE Feedback Eliminator (FBE)
Using the DARE FBE: How and Where
Notes: Note: Offline mode allows the viewing of the Fixed filters and settings. Must be connected to see dynamic information.
Note: Up to 8 Processing Blocks with FBE per DSP in the system.
Note: “Q” is a measurement of the notch width of each filter node. Higher Q = a narrower notch of frequencies.

## Slide 9
Where can the DARE FBE be implemented?
BMA 360
Standard Mic Inputs
Wireless DIALOG 20 Inputs
Dante Receive Channels
DARE Feedback Eliminator (FBE)
Between any Microphone Input and any Speaker Output
Notes: Note: Best practices, as outlined here, are for each BMA360 is to include a Processing + FBE channel in the local audio path.
Note: CONSOLE AI provides full routing flexibility to process audio for voice lift with no impact to what the remote location hears.

## Slide 10
Saves time – no manual tuning and re-tuning
Protects equipment from damage
Delivers impeccable audio for sound reinforcement with the BMA 360 and ClearOne’s other outstanding products
In Summary, the DARE FBE…
It’s All About the Architecture!
DARE Feedback Eliminator (FBE)